## Slide 1
C-HASAC: Contextual Heterogeneous-Agent SAC
for Decentralized 5G Power Coordination via Learned Latent Context
Yi-Chieh Hong, Yen-Ting Kuo, Wen-Ju Chiang
WinLab, National Yang Ming Chiao Tung University (NYCU) · 535518 Deep Learning Final Project, 2026
National Yang Ming
Chiao Tung University
Background & Motivation
• 5G multi-cell networks: inter-cell interference degrades PF fairness.
• Goal: maximize Proportional-Fair utility across all UEs:
U = Σu log( R̄u + ε )
• O-RAN constraint: each gNB observes only local UE metrics at runtime.
No direct neighbor CSI exchange is permitted.
• RIC xApp computes latent context z from KPM measurements
and pushes to gNBs via E2 interface — coordination without CSI leakage.
── O-RAN: RIC ↔ E2 ↔ BS1 / BS2 / BS3 (KPM↑, z↓) ──
Architecture
Three-Layer Information Flow (strict separation)
A
BS-local obs: per-UE {rate, PF weight, power} → Actor input (gNB-measurable in O-RAN)
B
RIC KPM: {load, throughput, P_BS, BS-distances} × 3 → Encoder → z[16] → all Actors
C
Privileged: full CSI g-matrix → Critic + reward (training only, never deployed)
Model Flow
KPM [3×5]
Encoder (MLP→pool)
z [16]
→ broadcast to all Actors
→
→
→
local obs [N_UE,i × 3]
+ z
SetActor (perm-equivariant)
power ≤ P_max
→
ONLY DIFFERENCE: C-HASAC actor receives z | HASAC actor does NOT
HASAC: Sequential Soft Policy Decomposition (Liu et al., ICLR 2024 §3.3)
Each BS updates in random permutation order → converges to QRE
(Quantal Response Equilibrium = global MaxEnt optimum, not sub-optimal NE)
Empirical: sequential HASAC −2.581 vs simultaneous −5.184 (+2.6 PF-U ✓)
Experimental Setup
Simulation (DeepMIMO)
• N_BS = 3, N_UE = 12
• Per-BS sum-power ≤ P_max
• Best-signal cell association
• Episode length T = 10 steps
Model & Training
• z_dim=16, kpm_dim=5
• share_dim=63 (critic)
• Hidden=256, SAC Twin-Q
• BC warm-start 1000 steps
• μ-bound=5 (tanh anti-collapse)
Evaluation Metric: PF-Utility (50 held-out episodes)
U = Σu log( R̄u + 10⁻⁶ )
−5.332
Floor (equal power)
−1.162
Best C-HASAC (400k)
+23.529
Ceiling (PF-WSR)
Results
+1.42 PF-U
Gain: C-HASAC − HASAC
+2.278
drop_shuffle (400k)
−1.162
Best C-HASAC PF-U
Method
PF-U (↑)
drop_zero
drop_shuffle
Note
Equal Power
−5.332
—
—
Floor
HASAC (no z, seq 400k)
−2.581
—
—
Sequential
C-HASAC geo_z (200k)
−2.237
+0.932
+1.429
—
C-HASAC + RSRP
−3.763
+0.688
+0.261
z ignored
C-HASAC + Critic BC
−2.606
−4.269
−0.453
z harmful
C-HASAC geo_z (400k) ★
−1.162
+3.565
+2.278
400k, BEST
PF-WSR oracle
+23.529
—
—
Full-CSI
Z-Ablation: drop_shuffle by Configuration
+1
+2
+1.43
geo_z 200k
+2.28
geo_z 400k ★
+0.26
+RSRP
−0.45
+Critic BC
Analysis & Discussion
Why z works (geo_z)
• BC warm-start unlocks z:
pure RL → drop_shuffle ≈ 0
+BC 1000 steps → +2.278 ✓
• KPM with BS distances →
z encodes spatial topology
• drop_shuffle > drop_zero →
z content used, not offset
• 400k > 200k: +1.43 → +2.28
Why ablations fail
• +RSRP: actor gets neighbor
channel gains → z ignored
+1.43 → +0.26 (unused)
• +Critic BC: encoder learns
to satisfy pre-trained Q,
not actor → z misleads policy
drop_shuffle = −0.45 ✗
Open Problem: SAC Q-Overestimation
• Peaks at step ~40–80k then oscillates — max operator amplifies estimation error.
• Mitigated: μ-bound=5 + logpf reward + BC warm-start.
• Future work: Conservative Q-Learning (CQL) penalty.
Conclusion
✅ C-HASAC > HASAC by +1.42 PF-U (−1.162 vs −2.581, 400k steps).
The only difference: actor receives learned latent context z.
✅ z is genuinely used: drop_shuffle = +2.278.
Mismatched z hurts more than zeroing — content matters.
✅ BC warm-start is the key catalyst (pure RL → drop_shuffle ≈ 0).
1000 expert imitation steps opens the z-usage switch.
✅ O-RAN deployable: RIC xApp → E2 interface → gNBs.
No direct inter-BS CSI exchange required at runtime.
⚠️ Gap to PF-WSR ceiling (+23.529) remains; future: CQL for Q stability.